ARCHITECTURAL SPECIFICATION GUIDE

PRODUCT:

SECTION 02791

SURFACE SYSTEMS – RUBBER SAFETY TILE

PART 1 – GENERAL

  - SUMMARY

- Provisions of Division 01 apply to this section.

- Section includes the following types of playground surface sytems and accessories:

    - Cushioned resilient playground safety tile system.

- Related Sections:

    - Section 02230:  Site Clearing.

    - Section 02315:  Excavating, Backfilling & Compacting.

    - Section 02319:  Base Course.

    - Section 02630:  Storm Drainage System.

    - Section 02881:  Playground Equipment & Structures.

  - REFERENCES

- The publications listed below form a part of this Specification to the extent referenced.  The publications are referred to in the text by basic designation only.

- American Society for Testing and Materials (ASTM).

  - ASTM F-1292:  Impact Attenuation of Surface Systems Under and Around Playground Equipment.  (Included are test results for each different fall height.)

  - ASTM F-1487:  Playground Equipment for Public Use.

  - ASTM F-1951:  Determination of Accessibility of Surface Systems Under and Around Playground Equipment.

  - ASTM E648-95a:  “Standard Test Method for Critical Radiant Flux of Floor Covering Systems Using a Radiant Heat Energy Source.” (Flammability test.)

  - ASTM E303-98:  Skid Resistance in accordance with the procedures outlined in the ASTM Test Method E303-98 (test on rubber surfacing, both wet & dry).

  - ASTM C67 & ASTM D573:  Perform evaluation for shock absorbing properties in accordance with ASTM F-1292-99, using 50 freeze-thaw cycles as per ASTM C67 followed by 7 days exposure at 200F per ASTM D573.

- Federal Standards

  - FED-STD-795 (4/1/88) Uniform Federal Accessibility Standards (UFAS).

- Code of Federal Regulations (DFR)

  - CFR 28 Part 36 (1991) Nondiscrimination of the Basis of Disability by Public Accommodations and in Commercial Facilities, Final Rule.

- U.S. Consumer Product Safety Commission (CPSC)

  - CPSC (2008)  Handbook for Public Playground Safety, U.S. Consumer Product

Safety Commission, Washington, D.C.  20207, Telephone (310) 504-0494.

  - SPECIFIC DEFINITIONS

- Critical Height:  Standard measure of shock attenuation.  According to SPSC No. 325, critical height is defined as “the fall height below which a life-threatening head injury would not be expected to occur.”

- Fall Height:  According to ASTM F-1487, fall height is defined as “the vertical distance between a designated play surface and the protective surfacing beneath it.”  The fall height of playground equipment should not exceed the critical height of the protective surfacing beneath it.

- SBR:  Styrene butadiene rubber.

- Use Zone:  As defined by ASTM F-1487.

  - SUBMITTALS

- Coordination Drawings:  Layout plans and elevations drawn to scale for the coordination of playground equipment with playground surface systems.  Indicate playground equipment locations, use zones, fall heights, extent of protective surfacing, depths of material, and critical heights, sub-base materials, hardware, edge details, and drainage.

- Shop Drawings:  For each Playground Safety Tile surface system, included materials, cross sections, drainage, installation, penetration details, and edge termination including border edge.

- Color Samples for Initial Selection:  Manufacturer’s color charts or 4-inch squares of units (samples) indicating the full range of colors available.  Special order selections to be ordered with a 6 week lead-time.

- Color Samples for Verification:  for the following products, for each type of exposed finish required, prepared on Samples of size indicated below and of same thickness and material indicated for the Work.  If finishes involve normal color and texture variations, include Sample sets indicating the full range of variations expected.  Submit a minimum 4 inch x 4 inch square (4” x 4) Sample of the Tile Color selected.

- Submit manufacturer’s descriptive data and installation instructions, including cleaning and preventive maintenance instructions.

- Submit a list of materials and components to be installed as part of the system, by weight and/or volume and recommended coverage, including manufacturer’s name, shipment date, storage requirements, and precautions, and that shall state chemical composition and test results to which material has been subjected in compliance with these specifications.

- Submit a listing of at least 5 installations where products similar to those specified are installed and have been in successful service for a minimum period of 3 years.  This list shall include owner, address of installation, service or maintenance organization, date of installation, contact person, and phone number of the contact person.

- The Safety Tile manufacturer shall submit a signed statement attesting that the surfacing meets the requirements of ASTM F-1292 for a head-first fall from 2’ and shall provide a Certificate of Compliance from the International Play Equipment Manufacturers Association.

- The authorized manufacturer’s representatives shall certify upon completion of the installation that the safety surfacing has been installed in accordance with the manufacturer’s instructions and complies with the Contract Documents.

- A Certificate of Insurance shall be provided by manufacturers of Playground Safety Tile Resilient Surfacing Systems, covering both product and general liability, of not less than $1,000,000.  The issuing underwriter shall be AA rated.

- Maintenance Data:  Submit maintenance and repair manuals for playground tile surface systems.

  - PERFORMANCE REQUIREMENTS

- Safety:  Safety surfacing shall meet or exceed the performance requirements of ASTM F-1292 that a surface yield both a peak deceleration of no more that 200g, and a Head Injury Criteria (HIC) value of no more than 1,000g, for a head-first fall from the highest accessible portion of fitness equipment being installed.  The highest accessible portion of fitness equipment shall be as specified in Section 02881 Playground Equipment and Structures.  The installer is responsible for obtaining a determination from the safety surfacing manufacturer of the required product depth to meet the performance requirements for all play equipment.

- Certificates of Compliance:

    - The impact attenuation performance of the Safety Tiles proposed for installation shall be documented by certificated of compliance, as specified in sub-sections 1.04 A.5 and 1.04, A.6.

- Accessibility:

    - Safety Tiles intended to serve as accessible paths of travel for persons with disabilities shall be firm, stable and slip resistant and shall meet the requirements of FEDSTD 795, 28CFR Part 36, ASTM F-1487, ASTM F-1487, ASTM F-1292, and ASTM F-1951-99.

  - QUALITY ASSURANCE

- Comply with the following as a minimum requirement:

    - Source Limitations:  Provide secondary materials including adhesives, anchoring materials, filler/sealant materials, and repair materials of type and from source recommended by manufacturer

  - COORDINATION

- Coordinate installation of safety tile to precede installation of fitness equipment, including accurate use zones and fall heights, specified in Section 02881:  Fitness Equipment and Structures.

  - DELIVERY, STORAGE, AND HANDLING

- Deliver manufactured materials in original package with seals unbroken and bearing manufacturer’s labels.

- Store manufactured materials in a clean, dry location, protected from the weather and deterioration, and complying with manufacturer’s written instructions for minimum and maximum temperature requirements for storage.

- Store units on flat surfaces.

1.09  PROJECT CONDITIONS

- Environmental Limitations:  Do not install safety tile over wet or excessively damp substrates if prohibited by manufacturer’s written instructions.

- Weather Limitations:  Proceed with installation only when existing and forecasted weather conditions permit playground tile system to be installed according to manufacture’s written instructions.

- Field Measurements:  Where safety tile is indicated to fit to other work, verify dimensions of other work by field measurements prior to installing the work of this section.

- Adhesives:

    - Install adhesives only when temperatures of surfaces to be adhered to and ambient air temperatures are within range permitted by manufacturer’s written instructions.

    - Close area to traffic during tile surfacing installation and for time period after installation as recommended by manufacturer.

    - Do not install products over concrete slabs until slabs have cured and are sufficiently dry and surfaces are within acceptable pH range to bond with adhesive, as recommended by surfacing manufacturer.

- Playground Safety Tiles

    - Install Safety Tile system only when ambient air temperatures during installation and for time period after installation are within range permitted by manufacturer’s recommended procedures.

    - Close area to traffic during installation and for time period after installation as recommended in manufacturer’s recommended procedures.

    - Protect Safety Tiles and adjacent materials (accessories: Edge pieces {“Ramps”}, corner pieces, adhesive, clips, etc.) from damage and exposure to adverse weather conditions.

PART 2 – PRODUCTS

  - MANUFACTURERS

- Manufacturers:  Environmental Molding Concepts

- Contact: 14050 Day Street · Moreno Valley, CA 92553 (888) 836-2665, www.emcmolding.com

  - SAFETY TILE, GENERAL

A. Accessibility: Provide a safety tile surfacing system determined to be    accessible when tested according to ASTM F-1951 and designed to comply with requirements for an accessible route as recommended by ADA Accessibility Guidelines.

  - RUBBER TILE FLOOR SYSTEMS

- General:  Provide surfacing designed to drain freely according to manufacturer’s recommended procedures as follows:

  - Substrate and Substrate Systems:

a.	Verify	manufacturer’s specifications for recommended procedures

for specific instructions on applicable substrate.

  - Acceptable substrates include asphalt, concrete, and compacted stone as listed and/or recommended by the manufacturer.

  - Other substrates shall be as permitted by the manufacturer before installing the Work of this section.

  - Substrate Acceptance:  Verify that the substrate and edge conditions are

acceptable and are in accordance with the manufacturer’s specifications.

- Materials:  EquiTile

  - 100% post-consumer recycled SBR (Styrene Butadiene Rubber) and pigmented with polyurethane.

  - Thickness & Weight: 1”, 3.875 lbs/sq.ft.

  - Color: [Red, Blue, Black, Green, Gray, Brown, Blue/Black, Gray/Black, Green/Black, Brown/Black, Red/Black]

- Accessories:  Supply accessories as required to complete the installation according to specified requirements and project drawings.

  - Sure Stick Adhesive

  - SportPlay Ramp

  - Kid Konnector Pins

PART 3 – EXECUTION

3.01		MANUFACTURER’S INSTRUCTIONS

- Comply with instructions and recommendations of the playground surfacing manufacturer

  - EXAMINATION

- Site Verification of Conditions: Verify that substrate conditions are suitable for installation

of the playground surfacing system.

- Do not proceed with installation until unsuitable conditions are corrected.

  - PREPARATION

- Surface Preparation:  Ensure that the concrete or asphalt substrate is level or uniformly sloped since surface variations will be telegraphed through to the rubber tile surface

  - INSTALLATION

- Do not proceed with surfacing installation until all applicable site work and other relevant work, has been completed.

- Insure that the substrate is clean, level, and dry.  Tiles must be dry.

- Check ambient air temperature.  Minimum temperature for installation is 50 degrees F and rising.  SportPlay Tiles are manufactured to 24” X 24” dimension plus or minus 1/8”.  Tiles should be checked prior to installation to ensure that the tiles are properly conditioned.  Tiles with dimensions smaller than 23 7/8” or larger than 24 1/8” must be conditioned prior to installation.  Installing tiles that are larger than 24 1/8” (hot weather) will result in “gapping” between tiles when the ambient temperature cools.  EMC is not responsible for gapping that occurs due to high temperature conditions at the time of installation.

- Refer to Manufacturers Installation Recommendations.

  - PROTECTION

- Protect the installed surface from damage resulting from subsequent construction activity on the site.

End of Section